## Slide 1: serial robots

## Slide 2: metronomes
produce audible click or other sound at a regular interval

## Slide 3: my project
build own metronome
use microcontroller and accessory board

## Slide 4: “GUI”
display values
change volume
speaker
LED
toggle mode, change beats per bar
change bpm
beats per bar
current beat
mode

## Slide 5: inputs
digital buttons  EXTI
potentiometers  ADC
Button press triggers FLAG for button. While loop triggers action, if a certain FLAG is set.

## Slide 6: outputs
display  given LCD driver using SPI
LEDs  GPIO
speaker  PWM signal

## Slide 7: tasks
void update_volume();
void update_bpm();
void update_display();
void button_push(); // check flags
void beat_machine(); // beep and blink
What is most important? What can wait?
timing not so important
timing absolutely important

## Slide 8: program flow
void update_volume();
void update_bpm();
void update_display();
void button_push(); // check flags
void beat_machine(); // beep and blink
What is most important? What can wait?
WHILE LOOP
TIMER INTERRUPT

## Slide 9: some important functions

## Slide 10: update_bpm() function
read analog input
calculate bpm within defined range (40 - 200 bpm)
calculate new prescaler value
set new prescaler value using TIM6->PSC

## Slide 11: external interrupts (buttons)
one task: set flags

## Slide 12: button_push() function
checks button flags
acts if a flag is up
resets flag

## Slide 13: beat_machine() and beat functions
normal beep
every 1st beat has higher pitched beep
STANDARD
PRONOUNCED
What mode is active?
beat_machine()
increment beat
beat += 1
or beat = 1

## Slide 14: results / demonstration